## Slide 1: FaultDetective Explainable to a Fault, from the Design Layout to the Software
Zhenyuan (Charlotte) Liu, Dillibabu Shanmugam and Patrick Schaumont
WPI Vernam Lab
CHES 2024
September 2024

## Slide 2: Outline
What is Fault Root-Causing?
Current Fault Research
Dynamic State Transition Graph
Visualized Fault Patterns
Fault Root-Cause Analysis: FaultDetective
Fault Root-Cause Demonstration
Conclusion

## Slide 3: What is Fault Root-Causing?
Explain Low-level Hardware Effects from High-level Software Observations
High-Level
Software
Low-Level
Hardware
Fault Effects
Fault Injection
2
Why do we care?
Faulty output
No effects
Halted CPU
We aim to understand more than just the immediate output effects!
Initial fault
Fault propagation
Impacts
Improved design
Cost Savings

## Slide 4: Current Fault Research
Simulation-based research:
  Based on a fault model of the design under test
  Includes bit flipping, permanent faults, gate modifications, instruction skips, etc
  Assumes specific locations of faults
  Can explain low-level details but depends on the accuracy of the fault model, which may be incorrect
Empirical research:
  Observes the real-world effects of faults
  Limited visibility into low-level hardware details
  Cannot explain the effects of faults at a high-level in software
Bridge this gap
Locate fault root-cause
Track fault propagation
Visualize fault behavior
3
FaultDetective

## Slide 5: Architecture and Micro-Architecture States
4
High-Level FSM
Software
Hardware
ISA
TOP-A
Top
W1
W2
Word
scan_in
scan_out
Bit
TOP-M
Top
W1
W2
W3
W4
Word
M1
M2
Module
  Programmer Visible Bits
  Programmer Visible Bits
  Programmer Non-Visible Bits
Architecture State
Micro-Architecture State
Architecture
Micro-Architecture

## Slide 6: Hierarchical Hash Tree
Micro-Architecture State
Architecture State
5
ISA
TOP-A
Top
W1
W2
Word
scan_in
scan_out
Bit
TOP-M
Top
W1
W2
W3
W4
Word
M1
M2
Module
Architecture
Micro-Architecture
Hierarchical tree structure (leaf/root)
Any changes at a leaf node will result in a change at the root node
Backtrack from the root node to identify which leaf or intermediate node is faulty
Hash tree [1]
Root node
Leaf nodes
Intermediate nodes
Intermediate nodes
Root node
Intermediate nodes
Architecture State Digest
Micro-Architecture State Digest
Any changes from leaf/intermediate nodes will cause a different hash value in the root digest
Find the root-cause of the fault
[1] please refer to our paper to find more details on the hash function.

## Slide 7: Dynamic State Transition Graph
6
ISA
TOP-A
Top
W1
W2
Word
scan_in
scan_out
Bit
TOP-M
Top
W1
W2
W3
W4
Word
M1
M2
Module
Architecture
Micro-Architecture
  Architecture Dynamic State Transition Graph (ADSTG)
  Micro-Architecture Dynamic State Transition Graph (MDSTG)
A1
A2
  Per Instruction
M1
M2
  Per Cycle
Track the system behavior in graphs!
  Programmer Visible Bits
  Programmer Non-Visible Bits
Architecture State Digest
Micro-Architecture State Digest

## Slide 8: Dynamic State Transition Graph – Before Fault
7
Architecture state
Transition time
Micro-architecture state
Sane State Achieved in accordance with the programmer’s intent[1]
The Sane Machine The collection of all possible sane states
[1] Thomas Dullien. Weird machines, exploitability, and provable unexploitability. IEEE Transactions on Emerging Topics in Computing, 8(2):391–403, 2020.
Pre instruction transition
Pre cycle transition
Programmer visible bits
All bits

## Slide 9: Dynamic State Transition Graph – After Fault
8
@29
Register R2 03 13
Disables further instruction-fetch
Halt the processor
[1] Thomas Dullien. Weird machines, exploitability, and provable unexploitability. IEEE Transactions on Emerging Topics in Computing, 8(2):391–403, 2020.
Transition time
Architecture state
Micro-architecture state
Weird State The behavior that occurs
when the sane state enters an otherwise
unreachable state[1]
The Weird Machine The collection
of all possible weird states
Visualize sane machine
Visualize weird machine
Assist in the fault analysis
Initial fault and its propagation
Architecture sane state
Micro-architecture sane state
Micro-architecture weird state
Architecture weird state

## Slide 10: Visualized Fault Patterns
Four fault patterns
9
States
Weird machine does exist!

## Slide 11: Fault Root-Cause Analysis: FaultDetective
Hardware Redundancy + Scan Chain
10
Processor
Peripherals
Memory
Registers
Core
Core
Core
Core
Core
Core
On-chip Network
Scan In
Scan Out
Lock-step execution
Minimal hardware in
on-chip network
Fault checking in software
by redundancy
Once a fault is detected,
halt all cores
Scan chain provides visibility
into all flip-flop bits

## Slide 12: Fault Root-Cause Analysis: FaultDetective
11
Plot the ADSTG/MDSTG for both sane and weird machine
Apply to both simulation and measurement fault experiments
Fault Detection by Software Redundancy
Fault root-cause
Software
Assembly
Hardware
Verilog
Time
Fault Injection
Fault propagation
Scan states over time after fault
Scan
States
Initial fault (root-cause)
Detect differences among cores
Earliest fault detection
Document all register bits
periodically

## Slide 13: Layout-Aware Fault Analysis in Simulation
Realization in ASIC (six-core MSP430)
Implement real-world fault injection using layout data (laser and clock fault injections)
No assumptions about the fault
12
RAM
CORE0
CORE1
CORE2
CORE5
CORE4
CORE3
Scan In
Scan Out
Layout Distribution
X-coordinate (𝝁𝒎)
Y-coordinate (𝝁𝒎)
Selected Region
Register Bit
Layout P&R
Laser Spot Size = 15

## Slide 14: Fault Root-Cause Demonstration – Before Fault
VerifyPIN5
// Hardcoded user PIN
#define USER_PIN_0 0x01
#define USER_PIN_1 0x02
#define USER_PIN_2 0x03
#define USER_PIN_3 0x00
// Hardcoded card PIN
#define CARD_PIN_0 0x01
#define CARD_PIN_1 0x02
#define CARD_PIN_2 0x03
#define CARD_PIN_3 0x04
Architecture sane state
Micro-architecture sane state
Transition time
Use one single fault to bypass the pin verification process
Return True

## Slide 15: Fault Root-Cause Demonstration – After Fault
Break the countermeasure
Clock glitching
@173
Cause the instruction sequencer to skip two instructions
Skipped
Skipped
Terminates the trial counter test
g_ptc
Hardened Boolean is not implemented
Any positive value compromises the countermeasure

## Slide 16: Conclusion
FaultDetective can:
  Achieve real-time fault detection at the earliest possible moment using hardware redundancy
  Identify the earliest onset of a fault using a scan chain
  Track fault propagation through a scan chain
  Monitor system behavior using graphs (ADSTG/MDSTG)
  Assist in the precise analysis of application failures
  Bridge the gap between fault simulation based on fault models and fault testing based on real experiments
15
FaultDetective
This research was supported in part by

## Slide 17: Any Questions?
Thank you
zliu12@wpi.edu

## Slide 18: Realization in ASIC
Six MSP430 Cores
Total scan bits: 1702*6 = 10212
Micro-architecture of one core MSP-430 Micro-architecture
17

## Slide 19: Simulation Results
18

## Slide 20: Fault Root-Cause Example
Target Firmware with fault pattern examples
19

## Slide 21: Fault Root-Cause Demonstration – Before Fault
20
A loop that only includes case0
A roundtrip of every 41 clock cycles

## Slide 22: Fault Root-Cause Demonstration – After Fault
21
Suppose to execute F03E and proceed
Now jumped to F038
Clock glitching
@13
PC register is faulted from F03E to F038 (jump backward)
F038: cmp r12 r12
Faulted the case decoding instruction
switch(state)

## Slide 23: Fault Root-Cause Demonstration – After Fault
22
F038: cmp r12 r12
A loop that only includes case0
Now entered case2!

## Slide 24: Design-Layout Aware Simulation Framework
23
Post-Syn Netlist with Software Binary
Post-Layout SDF
Design-layout Aware Fault Simulation
Signal
Activities
Simulation Tool
Multi-core Faulty Scan States
Weird Machine Analysis
Python
Fault Root-cause Analysis
Scan State
Differential
&
Graph Generation
ADSTG
MDSTG
Layout Data
Fault Parameter Generation
Fault Parameter in Testbench
C Code, Assembly, RTL Verilog
Python
Ground Truth
Fault
Detected
Choose
One
As the
Ground
Truth
Majority Voting
(posteriori)
Golden Scan
(priori)
Root-Cause
Non-faulted Scan States
Framework