## Slide 1
Hierarchical Side-channel Leakage Assessment for Post-Quantum Cryptographic Accelerators
Patrick Schaumont 9/30/25
Notes: This PowerPoint Template includes a series of slide masters with predefined layouts and color schemes for formatting slides
Slide Masters are displayed when you right click on a slide and select Layout from menu

## Slide 2: Why Hierarchical PSLA for RoT (ML‑DSA‑87)?
Secure algorithm ≠ secure implementation
Find leakage early in the design cycle.
Trace root causes across Arch → µArch → Gate
Fixes are cheaper and less risky pre‑tape‑out.
Arch PSLA
mArch PSLA
Gate PSLA
Prototype
Arch Leakage
Secure Design (SW + RTL)
Emergent uArch Leakage
Emergent Logic Leakage
Measurement
Logic
Synthesis
Backend
Parasitics
Hierarchical PSLA
Post-silicon SLA
Gate Root Cause
mArch Root Cause
Arch Root Cause
FIX
FIX
FIX
Notes: Secure algorithm ≠ secure implementation
RoT anchors boot, attestation, identity
leakage breaks trust
Why Pre-silicon Leakage Assessment(PSLA)?
Detects weaknesses before tape-out
Fixes are cheapest at this stage
Why Hierarchical PSLA?
Large, long-running accelerators
Leakage can be progressive, disappear, or emerge
Requires cross layer analysis

## Slide 3: Black‑box vs White‑box testing
Cryptographic
Algorithm
Designer
Studied by
Implements
Tester
Black
Box
Properties
Considered
by
measures
Classic measurement scenario
Operation Selection
ISA with Extensions
Micro-architecture Design
Gate-level Design
Simulator‑driven PSLA scenario
Predicts
leakage
Tester
Simulator
Early
Feedback
White‑box PSLA delivers early feedback
by estimating leakage

## Slide 4: Toggle-based Pre-silicon Simulator
D
Adams Bridge RTL
mldsa wrapper
memory
Testbench
Gate level
wrapper
Replay
Signature
Signature same?
Toggle
monitor
Dynamic power ≈ α·C·V²·f; Dynamic power ∝ switching activity (α)
Capture cycle‑accurate toggles (VCD/SAIF) from RTL and gate‑level simulation
Treat toggle counts as the power/EM proxy for leakage testing
Notes: - Cycle‑accurate toggles preserve the same functional dependence on data as post‑silicon power/EM (up to noise and constant operations overheads).
- Use per‑register toggle features as attack traces; center/align per experiment; run CPA/2oCPA/template.

## Slide 5: RTL vs Gate Level Summary
RTL
    2 minutes for an mldsa sign operation
Gate Level
    RAM modules are synthesized as black-box​
    Gate-level model on IHP13, TSMC180​
 | IHP13 | TSMC180
RAM | 10 | 10
Flip Flop | 273,701 | 273,363
Comb + Flip Flop | 1,153,569 | 824,942
Cell Area (sqmu) | 26,338,600.335 | 20,146,217.239
Simulation(Time) | 7 hours | 15 hours
Challenge: scaling correlation, TVLA to full design

## Slide 6: ML-DSA-87: Point of Interest
Signing :
To sign a message M ∈ {0,1}*,
Alice does:
Compute c = H(M || w).
Compute z = y + cs₁.
Output σ = (c, z).
w is commitment
c is challenge
z is response
c.s1 is critical security parameter
s1 is secret
The coefficients have 23 bits
Number-Theoretic Transform(NTT)
Z = NTT(c) * NTT(s1) * is point-wise multiplication(PWM)
This step is vulnerable to side‑channel attacks.
Notes: Alice’s verification key is (A, t),
where A ∈R and t = As₁ + s₂
where s₁ ∈R and s₂ ∈R
Alice’s signing key is (s₁, s₂).

## Slide 7: PSLA : Unprotected point-wise multiplication
Z = c.s1
We collect toggle counts of the register holding Z = c⋅s1 as a power proxy
Correlate with a hypothetical power model

## Slide 8: PSLA: Masked two-share PWM (2s-PWM)
S1 - m1​
m1​
r
C - m2​
m2​
D0​
D1​
C1​
C0​
Z1​
Z0
Masked 2-share product Z = C⋅S1 (mod q)
q is 8380417; S1 is secret; C is known;
mask variables : m1, m2; refresh : r
HDt1 = HD(C0) + HD(D0) + HD(C1) + HD(D1)
HDt2 = HD(Z0) + HD(Z1) HD = Hamming Distance
L product = HDt1 * HDt2 L abs diff = abs (HDt1 - HDt2 )
L sum of sq = (HDt1 * HDt2 + HDt1 * HDt2 )
Second order leakage models
t1
t2
Expose coupling in masked data paths

## Slide 9: Results: Key Rank and Traces
Distinguishers | Traces (MTD)
CPA (PWM) | 6
SOCPA (2S PWM) | 10250
Template (2S PWM) | 55
Our analysis identified successful second‑order attacks on masked PWM
Traces | Key rank (23bit) |  | 
 | L product | L abs diff | L sum of sq
6 | 1 | 1 | 1
10250 | 163 | 147 | 1
55 | 5 | 1 | 1
MTD by distinguisher
Key rank vs traces​

## Slide 10: Parallel 2S‑PWMs: Randomness Reuse Weakness
Masks m1,m2 identical across instances (→ same C1 ).
Randomness reused in two instances (white)
Result: partial key recovery for those instances.
C0
D0
D1
C1
Z0
Z1
C0
D0
D1
C1
Z0
Z1
C0
D0
D1
C1
Z0
Z1
C0
D0
D1
C1
Z0
Z1

## Slide 11: Plan for Next Phase
Gate‑level PSLA
  build efficient simulator
  define gate‑level distinguishers
  account for multiple leakage sources of CSPs.
Cross-layer Analysis
  Hierarchical PLSA with outcome matching across levels
Identify a module for tape out

## Slide 12: Selected References
Cross-layer Analysis
  Z. Liu, A. Malnicof, A. Roy, P. Schaumont: Telescope: Top-Down Hierarchical Pre-silicon Side-channel Leakage Assessment in System-on-Chip Design. 20th ACM ASIA Conference on Computer and Communications Security (AsiaCCS 2025), August 2025, Hanoi, Vietnam.
  * M.-J. O. Saarinen, “WiP: Applicability of ISO Standard Side‑Channel Leakage Tests to NIST Post‑Quantum Cryptography,” Cryptology ePrint Archive, Report 2022/229, 2022. [Online]. Available: https://eprint.iacr.org/2022/229.pdf
  Caliptra : Adams bridges https://github.com/chipsalliance/adams-bridge

## Slide 13: Project Schedule
Current Focus
Pending
Annual Review
Arna Roy
Dillibabu Shanmugam

## Slide 14
Thank you

## Slide 15: Cross-layer Analysis

## Slide 16: Cross Layer Analysis
Arch PSLA
mArch PSLA
Gate PSLA
Prototype
Arch Leakage
Secure Design (SW + RTL)
Emergent uArch Leakage
Emergent Logic Leakage
Measurement
Logic
Synthesis
Backend
Parasitics
Hierarchical PSLA
Post-silicon SLA
Gate Root Cause
mArch Root Cause
Arch Root Cause
FIX
FIX
FIX

## Slide 17: Matching the PSLA outcomes
High-Level Model (e.g. instruction- accurate)
Low-Level Model (e.g. cycle- accurate)
Leakage Test
Leakage Test
N
N
Design Refinement
Undecided
N
Y
False Negative
Y
N
False Positive
Leaky
Y
Y
Progressive Leakage

## Slide 18: Matching the PSLA outcomes
High-Level Model (e.g. instruction- accurate)
Low-Level Model (e.g. cycle- accurate)
Leakage Test
Leakage Test
N
N
Design Refinement
Undecided
N
Y
False Negative
Y
N
False Positive
Leaky
Y
Y
Progressive Leakage
Emerging Leakage

## Slide 19: Matching the PSLA outcomes
High-Level Model (e.g. instruction- accurate)
Low-Level Model (e.g. cycle- accurate)
Leakage Test
Leakage Test
N
N
Design Refinement
Undecided
N
Y
False Negative
Y
N
False Positive
Leaky
Y
Y
Progressive Leakage
Emerging Leakage
Disappearing Leakage

## Slide 20: Hierarchical Root causing
To demonstrate progressive side-channel leakage, we must establish a causal relationship between the SLA results at different abstraction levels
However, this cannot be achieved by looking at data alone (aka the plausible deniability problem of root-causing ..)
t-value
t-value
high
level
low
level
???

## Slide 21: Hierachical Root Causing through Dependencies
Architecture
Micro-architecture
Gate-level
Time (Cycles)
Time (Cycles)
Time (Cycles)
Intracycle Dependency Analysis
causes
a
a

## Slide 22: Hierachical Root Causing through Dependencies
Architecture
Micro-architecture
Gate-level
Time (Cycles)
Time (Cycles)
Time (Cycles)
Intercycle Dependency Analysis
b
c
b
c

## Slide 23: Defining the dependency
a dependency implies a timing path through digital logic
start point
register output
primary input
end point
register input
primary output
1 cycle
path elements
logic gates
wiring
reg1
reg2
gate1
gate2
gate3
dependency examples:
reg1 to reg2
gate2 to reg2
reg1 to gate3

## Slide 24: Example: Tracking Progressive Leakage
AES128_Encrypt:
...
lbu a4, 0(a4); load sbox[index]
sb a4, -1(a5); store in state
fix-vs-random test on a plaintext byte

## Slide 25: Example: Tracking Progressive Leakage

## Slide 26: Example: Tracking Progressive Leakage

## Slide 27: Example: Tracking Progressive Leakage
Gate Power Post Syn

## Slide 28: Adams Bridge PSLA

## Slide 29: Distinguishing features of the PQC PSLA
Analysis on very large implementation
  No architecture-level
  Micro-architecture level: 508,413 flip-flops in ML-DSA (+ 408,608 SRAM bits)
  Gate-leve: TBD

## Slide 30: Distinguishing features of the PQC PSLA
Analysis on very large implementation
  No architecture-level
  Micro-architecture level: 508,413 flip-flops in ML-DSA (+ 408,608 SRAM bits)
  Gate-leve: TBD
Multiple sources of leakage of CSPs*
* M.-J. O. Saarinen, “WiP: Applicability of ISO Standard Side‑Channel Leakage Tests to NIST Post‑Quantum Cryptography,” Cryptology ePrint Archive, Report 2022/229, 2022. [Online]. Available: https://eprint.iacr.org/2022/229.pdf
  Kyber
    Encrypt/Decrypt API
    Secret Key/ Public Key distinguisher
    Encapsulate/Decapsulate API
    Plaintext Checking
  Dilithium
    Sign/Verify API
    Message distinguisher
    Public/Secret Key distinguisher

## Slide 31: Distinguishing features of the PQC PSLA
Analysis on very large implementation
  No architecture-level
  Micro-architecture level: 508,413 flip-flops in ML-DSA (+ 408,608 SRAM bits)
  Gate-leve: TBD
Multiple sources of leakage of CSPs*
Very large activity footprint
  MLDSA signing takes 42,666 cycles creating a 24G VCD file
* M.-J. O. Saarinen, “WiP: Applicability of ISO Standard Side‑Channel Leakage Tests to NIST Post‑Quantum Cryptography,” Cryptology ePrint Archive, Report 2022/229, 2022. [Online]. Available: https://eprint.iacr.org/2022/229.pdf
  Kyber
    Encrypt/Decrypt API
    Secret Key/ Public Key distinguisher
    Encapsulate/Decapsulate API
    Plaintext Checking
  Dilithium
    Sign/Verify API
    Message distinguisher
    Public/Secret Key distinguisher
Main Analysis Challenge is on scaling up traditional testing techniques (Correlation, TVLA, ..) to apply to a very large design. Hierarchical top/down analysis will be essential.

## Slide 32: Starting Point
Pre-silicon Side-channel Leakage Assessment Model for ML-DSA
  Performs VCD toggle counting on RTL model
https://github.com/ml-dsa/abr-sim
https://github.com/chipsalliance/adams-bridge

## Slide 33: Planned Activities (next 3 months)
Planned Activities
  Rework testbench to do micro-arch level PSLA
  Build distinguishers for ML-DSA leakage testing
    Key generation
    Signature Generation
  Synthesize a gate-level model for gate-level PSLA
    Currently aiming at IHP SG13G2 (130nm) Open Source PDK with SRAM cells
  Extend testbench to do gate level PSLA

## Slide 34: Project Schedule
Current Focus
Pending
Annual Review
Arna Roy
Dillibabu Shanmugam

## Slide 35: Jun 11, 2025 Tapeout
180 MS RF G

## Slide 36: Discussion

## Slide 37: How much power detail do we need?
Vdd
Vss
R
A
B
Y
X
C
i
Early propagation & glitches
IR Drop
Capacitive coupling
Transitions
Substrate noise coupling
Static leakage
2
1
3
4
5
6

## Slide 38: How much power detail do we need?
Vdd
Vss
R
A
B
Y
X
C
i
Early propagation & glitches
IR Drop
Capacitive coupling
Transitions
Substrate noise coupling
Static leakage
2
1
3
4
5
6
Toggle
Gate Power Post Syn
Gate Power Post Layout
Signal/Power Integrity